## Slide 1
THE GENERATOR:
WHAT IS A GENERATOR?
IT IS A DEVICE THAT CONVERTS MECHANICAL ENERGY INTO ELECTRICAL ENERGY THROUGH ELECTROMAGNETIC INDUCTION. THE INDUCTION STATES THAT IF A CONDUCTOR IS MOVED IN A MAGNETIC FIELD, THE ELECTRIC CURRENT WILL FLOW IN THE CONDUCTOR.
WHAT IS MADE OF?
IT CONSISTS OF A LOOP OF WIRE (FASCIO DI CAVI), CALLED “ARMATURE” PLACED BETWEEN THE NORTH AND THE SOUTH OF A MAGNET (THE FIELD). THE ARMATURE ROTATES TO PROVOKE AN ELECTROMAGNETIC FORCE IN THE LOOP. AT THE END IT IS CONNECTED TO SLIP RINGS IN AC GENERATOR OR TO A SPLIT RING (THE COMMUTATOR) IN DC GENERATOR.
THESE RINGS ROTATE WITH THE ARMATURE AND THEY ARE CONNECTED TO THE EXTERNAL CIRCUIT THROUGH BRUSHES. AT THE SIDES OF THE LOOP TH EMF CAUSES A CURRENT TO FLOW THROUGH THE LOOP.

## Slide 2
THE MOTOR:
A MOTOR TRANSFORM ELECTRICAL ENERGY INTO MECHANICAL ENERGY WITH AN ELECTROMAGNETIC REACTION.
MOTOR ARE CLASSIFIED IN AC OR DC MOTORS.
AC MOTORS: THE CURRENT IN THE ARMATURE CHANGES POLARITY MOVING IN BOTH DIRECTIONS. IT IS ADVANTAGEOUS FOR ELECTRIC TRANSMISSION. AS TO PREVENT THE SPARKLING BETWEEN BRUSHES, THE ALTERNATORS ARE BUILT WITH A STATIONARY ARMATURE. THE GENERATED CURRENT MAY BE SINGLE-PHASE, THREE-PHASE.
DC MOTORS: THESE MOTORS NEED A COMMUTATOR TO PRODUCE DIRECT CURRENT. WHEN THE ARMATURE TURNS, THE COMMUTATOR CHANGE POSITION WHEN THE CURRENT REVERSE THE DIRECTION. THEY ARE USED AT LOW VOLTAGE TO PREVENT SPARKLING. MODERN DC GENERATORS USE DRUM ARMATURE, WITH A LARGE NUMBER OF WINDINGS, CONNECTED TO A COMMUTATOR. THIS ALLOWS A CONSTANT AMOUNT OF CURRENT.

## Slide 3
THE MOTOR: STRUCTURE
A motor consists of an ARMATURE (rotor) that is an electromagnet made by wires around a metal coil and of a stator (PERMANENT MAGNET). The ARMATURE has a SHAFT with a COMMUTATOR that provides the two connections for the coil of the EMT. Two pieces of metal, the BRUSHES, conduct the current to the COMMUTATOR.